Numerical simulation of the hydrodynamic functioning of the mouth of Bandama River, Côte d’Ivoire

Kouakou Lazare KOUASSI1, Kouakou Séraphin KONAN1, Moussa DEME2, Kouassi Innocent KOUAME3, N'diaye Hermann MELEDJE3, Diakaria KONÉ4, Martin SANCHEZ ANGULO5 and Kouamé AKA6

1Centre de Recherche en Ecologie, Université Jean Lorougnon Guédé, 08 BP 109 Abidjan 08 (Côte d’Ivoire) ; k_lazare@yahoo.fr;

2Département Infrastructures et Transport, Institut National Polytechnique Félix HOUPHOUËT-BOIGNY, BP 1083 Yamoussoukro (Côte d’Ivoire); deme_moussa@hotmail.com

3Centre de Recherche en Ecologie, Université Nangui Abrogoua, 08 BP 109 Abidjan 08 (Côte d’Ivoire) ; innocent_kouassi@yahoo.fr ; meledjendiay@yahoo.fr ;

4Office National de l’Eau Potable (ONEP), Direction des Ressources en Eau, Abidjan, Côte d’Ivoire ; konediak@live.fr ;

5Laboratoire de Planétologie et Géodynamique, Université de Nantes, Faculté des Sciences et des Techniques, Martin.Sanchez-Angulo@univ-nantes.fr

6Université Félix-HOUPHOUËT-BOIGNY, Abidjan, Côte d’Ivoire, akaraphael@yahoo.fr

Coastal erosion is a real problem in Côte d’Ivoire and particularly at the mouth of Bandama River in Grand-Lahou. It led to the transfer of Grand-Lahou City on the north part of this area in the 1970s. The erosion not only concerns the movements of the coastline but also the migration of the mouth of Bandama River westward, destroying habitats and plantations.

A hydro-sedimentological study was undertaken to support the construction of the channel of the fishing port in the mouth of Bandama River. This channel aims to ensure the navigability of the estuary of Grand-Lahou in order to revitalize the economy of this region.

The assessment of the migration speed of the pass and the simulation of the hydrodynamics of the mouth of Bandama River were conducted using satellite images, bathymetry survey, sediment characteristics and current velocities measured in June 2012.

Strongest currents are observed at the mouth Bandama River, in the pass and on either side of the central block. Currents are also important in the channel of Tagba Lagoon, where flow the largest water volumes.

In dry periods, the tide currents reach 1.4 m/s at the mouth of Bandama River and 0.4 m/s in the channel of Tagba Lagoon.
The mass of water bypasses the sandbanks and vases to join the main channel between the pass and the Tagba lagoon.

In flood conditions, high flow rates tend to block the ebb currents. Current velocities reach 1.8 m/s in the pass at the ebb tide and are reduced to 0.35 m/s at the rising tide. In Tagba channel tidal currents are lower at ebb tide (0.3 m/s to 0.4 m/s); the dynamics of tides are greatly reduced by high flows of Bandama River.